## Slide 1: ECE477 Midterm Design Review: Team 8
Notes: Introduce names.

## Slide 2: Outline
Project Overview
Major Components
Block Diagram
Packaging Design
Electrical Schematic
PCB Layout
Prototyping Progress
Software Development Status
Project Timeline
Questions

## Slide 3: Project Overview
Our project aims to simplify the process of applying audio effects to a guitar. It takes in the analog input from the guitar and uses digital signal processing to equalize audio output based on parameters from an Android App. Many products available in the market can transmit the guitar sound but lack the ability to add effects to the audio.
AudioBeamer
Artistic Rendering
Notes: CARSON

## Slide 4: PSSCs
The ability to interface with an external Audio Codec using I2S that delivers digital data sampled at a 16-bit resolution from an electric guitar and outputs analog audio.
The ability to use Bluetooth data received from an Android cell phone to control audio equalization on the Receiver PCB using UART.
The ability to apply audio effects & equalization such as bass, middle, treble, distortion, and reverb on digitally sampled audio using Digital Signal Processing.
The ability to use a developed Android app to pass user-customizable audio equalization data to the receiver MCU using inbuilt cell phone Bluetooth.
The ability to power the system using an external battery while being able to measure remaining battery levels using a coulomb meter and displaying it using an LED based UI.
Notes: SKIM OVER

## Slide 5: Major Components
MCU – Texas Instruments – MSP430FR5994
Audio Codec – PCM3002
Power management integrated circuit(PMIC) – STC3100IST
Linear Regulator – AP2127K-3.3TRG1
Lithium-ion Battery Charge Management Chip – MCP73837T-FCI/UN
Bluetooth Module – RN4020-V/RM
Audio Amplifier – LM4865
Total Current draw: 40 mA
  Amplifier may add up to 100 mA

## Slide 6: Major Components
We will use this to set up and communicate with peripheral devices and for DSP functions/operations
This has a Low-Energy Accelerator for Digital Signal Processing
Specifications
  16 MHz max system clock
  Supply voltage 3.3 Volt
    Recommended 1.8 - 3.6 Volts
  Typical current consumption 120 µA/MHz
    Max of 1.92 mA
  68 I/O
MCU – MSP430FR5994
Notes: CARSON

## Slide 7: Major component
Li-ion cell
Planning to use 2000mAh Li-ion cell
Expected battery life = 2Ah / 0.14A = 14.2 hours (Theoretical)

## Slide 8: Major Components
Can monitor voltage, temperature, current of a single-cell Lithium-Ion battery
We will use this to measure battery capacity to present to the user via an LED interface through the MCU
Specifications
  32 kHz clock
    Also has a I2C clock line
  Supply voltage 3.3 Volts
    Recommended 2.7 - 5.5 Volts
  Max current consumption 100 µA (typical not given)
  1 general purpose I/O
Power management integrated circuit – STC3100IST
Notes: CALVIN

## Slide 9: Major Components
A chip that supports Bluetooth Low Energy under Bluetooth specification version 4.1
We will use this component to get equalization, distortion, and reverb values from our Android app and send them to the MCU
Operating on UART with baud rate of 115,200 bits per second
Specifications
  Supply voltage 3.3 Volts
    Recommended 1.8 - 3.6 Volts
  Typical current consumption 16 mA
  7 I/O
    3 analog, 4 PWM
Bluetooth Module – RN4020-V/RM
Notes: CALVIN

## Slide 10: Major Components
Single-chip stereo audio codec with ADC and DAC lines
We will use this to input audio signals from an electric guitar to our MCU
Specifications
  48 kHz max sampling rate clock
    Using 44.1 kHz
  16/20 Bit Input/output Data
  Supply voltage 3.3 Volts
    Recommended 2.7 - 3.6 Volts
  Typical current consumption 18 mA
    Max is 24 mA
Audio Codec – PCM3002
"16/20-BIT SINGLE-ENDED ANALOG INPUT/OUTPUT STEREO AUDIO CODECS," October 2000. Online. Available: http://www.ti.com/lit/ds/symlink/pcm3002.pdf [March 2, 2020]
Notes: SOFTWARE INTERFACING – ADITYA T
3 wire SPI to program the mode control
Left justified I2S
Attenuation
Anti-aliasing
Mute

## Slide 11: Major Components
Capable of regulating voltage down to 0.8V to 5.5V
We will use this to guarantee a relatively constant voltage
Specifications
  Supply voltage 3.3 Volts
    Recommended 2.5 - 6 Volts
  Typical current consumption 60 µA
θja = 250 °C/W:
Maximum delta T = θja*(4.2V-3.3V) * (140 mA) = 33.75 °C => 58.75 °C @ max battery
  39 °C @ nominal battery (3.7V)
Low Dropout voltage – 170mV, will work for entire range of battery
Linear Regulator – AP2127K-3.3TRG1
Notes: ADITYA T

## Slide 12: Major Components
Linear Lithium-Ion/Lithium-Polymer battery charger
Specifications
  Supply voltage 3.3 Volts
    Recommended 0.3 - 6 Volts
  Typical current consumption 1900 µA when charging, 110 µA when charge complete, 75 µA on standby
    Max current (IC consumption) 3000 µA, 300 µA, and 100 µA respectively
    Auto cutoff
    Charge current of cell set at 0.1A (total 3000uA + 0.1A)
  θja = 113 °C/W
  Maximum delta T = θja*(5V-3.2V) * (0.1A) = 20.34 °C
LI-ion Battery Charge Management Chip – MCP73837T-FCI/UN
Notes: ADITYA T

## Slide 13: Block Diagram
Notes: ADITYA T

## Slide 14: Packaging Design
Notes: CARSON

## Slide 15: Electrical Schematic
MCU footprint too large to be shown on screen clearly
Notes: ADITYA B

## Slide 16: ELECTRICAL SCHEMATIC
Reset CIRCUIT
Followed the recommended circuit

## Slide 17: ELECTRICAL SCHEMATIC
BYPASS CAPACITORS ON MCU

## Slide 18: ELECTRICAL SCHEMATIC
EXTERNAL CRYSTAL – 16Mhz 18pF load capacitance
C = 2 * load capacitance – pin capacitance
C = 2 * 18pF – 2pF = 34pF
Pull up resistors for IO lines

## Slide 19: Electric schematic
Bootloader pins
Uses a UART based interface with
the dev-board

## Slide 20: Electric schematic – power system
Power system, battery charger, coulomb counter
Followed recommended circuit and joined them together

## Slide 21: Electric schematic
Bluetooth circuit – rn4020
Followed recommended circuit

## Slide 22: Electric schematic
Audio codec
Followed recommended circuit

## Slide 23: PCB Layout
Overall layout
Notes: ADITYA B

## Slide 24: PCB LAYOUT
MCU BYPASS CAPACITORS , RESET SWITCH & CRYSTAL

## Slide 25: PCB LAYOUT
ground plane shielding

## Slide 26: PCB LAYOUT
crystal
CRYSTAL GROUND PLANE

## Slide 27: PCB LAYOUT
POWER SYSTEM
Single LED for charge status
indication

## Slide 28: Pcb layout
Bluetooth module

## Slide 29: Pcb layout
Audio systems - PCM3002 AUDIO CODEC
Lots of capacitors!

## Slide 30: PCB LAYOUT
Audio systems
Using separate ground plane

## Slide 31: PCB LAYOUT
AUDIO SYSTEMS
Amplification circuit not designed yet
Should be implemented in a few days
Will manually solder wire to female ¼ audio jack
Mainly to avoid mounting jack on PCB

## Slide 32: Prototyping Progress

## Slide 33: PROTOTYPING PROGRESS
PARTIALLY COMPLETE
Test ability to set up and communicate with the Bluetooth module via UART (complete)
Test ability to set up and communicate with the audio codec via … (partially complete)
Test ability to set up and communicate with the PMIC via I2C and flash an LED accordingly (not started)
Test ability to apply equalization, distortion, and reverb effects to audio signals (barely started)
MCU – MSP430FR5594

## Slide 34: PROTOTYPING PROGRESS
PARTIALLY COMPLETE
Test ability to receive an audio signal from an electric guitar (not started)
Test ability to communicate with the MCU via … (partially complete)
Receive I2S output from a provided waveform (complete)
Still working on system & data clock synchronization
Amplification design & testing (not started)
Audio Codec – PCM3002

## Slide 35: PROTOTYPING PROGRESS
NOT STARTED
Test ability to be set up by and communicate with our MCU via I2C (not started)
Test ability to receive accurate voltage values from our battery (not started)
Power management integrated circuit – STC3100IST

## Slide 36: PROTOTYPING PROGRESS
FULLY COMPLETED
Test ability to communicate with Android APP via low energy Bluetooth (works)
Test ability to disconnect and unbind from previous devices (works)
Test ability to connect and bind to the Android app (works)
Test ability to receive data from the Android app to distinguish sliders from each other and the value sent (works)
Test ability to send data via UART to the MCU (works)
Test ability to be properly set up via UART by the MCU (works)
Bluetooth Module – RN4020-V/RM

## Slide 37: PROTOTYPING PROGRESS
BASICALLY COMPLETED
Test ability to communicate with Bluetooth module via low energy Bluetooth (works)
Test ability to connect and bind to the Bluetooth module indefinitely (works)
Test ability to send an integer value based on a slider for multiple sliders (works)
All further work done on this component will be UI improvements; all functionality is completed
Android App
Notes: CALVIN

## Slide 38: PROTOTYPING PROGRESS
POWER SYSTEM AND CHARGING CIRCUIT
ALMOST COMPLETED
Test ability to provide stable 3.3V DC to our system at up to 300mA (Complete)
Test ability to use a Li-ion cell to power the system reliably (Works in lab)
Test ability to charge Li-ion cell while providing power to our system (Complete)
Test analog ground separation circuit (ongoing)

## Slide 39: Software Development Status
Interfacing
  Bluetooth Low Energy (UART) - Completed
  Audio Codec – In development
  PMIC (I2C) - Not yet started
Android App
  Bluetooth Low Energy – Completed
  User Interface – Mostly Completed
Digital Signal Processing
  Equalization – In early development
  Reverb – In early development
  Distortion – In early development
Status by software category

## Slide 40: Software Development Status
Third party software
  Android Application
    Android.bluetooth
      Used to communicate to RN4020 (Bluetooth module)
      Utilizes Bluetooth Low Energy
    Android.widget
      Used to create GUI
      Includes text, sliders, and buttons
  MCU (MSP430)
    MSP DSP library
      Computations for equalization
      Computations for reverb
      Computations for distortion

## Slide 47: Project Timeline

## Slide 48: 3D Printing
Questions?